## Slide 1
Smart Waste Collector: Automatic Waste Management
Presented By- Group 03
1906143 – Md. Ali Ahmed
1906144 – Monideepa Kundu (Sinthi)
1906147 – Khondaker Nafis Ahmed
1906145 – Prantik Paul
1906148 – Tanzim Al Mahmud
1906146 – Aliva Sadnim Mahmud

## Slide 2
OVERVIEW
Key Features
Robotic Car Design
Robotic Arm Control
Trash Segregation
Trash Level Detection

## Slide 3
Key Features
Line Follower Robot
Robotic Arm
Trash Segregation
Trash Level Detection

## Slide 4
ROBOTIC CAR DESIGN (Hardware Part)
Designing the line follower robot.
Laser cutting ply-wood as per designed.
Buying and assembling necessary components.
Making appropriate connections to give power supply to every circuit component.
Connecting Arduino pins with circuit components for further software implementation.

## Slide 5
ROBOTIC CAR DESIGN (Software Part)
Writing code for the bot to follow line and make appropriate turns as per necessary. When the end of line is reached , the bot spins and searches for the line to return.
While finding trash on the line at an appropriate distance , the bot automatically stops and starts moving again when the trash has been picked up.
Implementing weight balancing and speed control.
Testing and debugging to make sure the bot works properly under adverse condition of the track.

## Slide 6
Video Demonstration

## Slide 7
Robotic Arm Control
Pitch Servo
Grip Servo
Elbow Servo
Roll Servo
Base Servo
Shoulder Servo

## Slide 8
Video Demonstration

## Slide 9
Trash Segregation (Metallic & Non-metallic)
Works based on the strength of magnetic field
Metal detector
Rotate 180 degree
No Rotation
Rotate 180 degree again
Receive Trash
If Metal
If Non- Metal
Detection range for different objects:
Switchblade- 5 mm
Battery- 15 mm
Metal Can -25 mm

## Slide 10
Trash Level Detection
Measure the distance to the target by measuring the time between the emission and reception
Detection range: 2 – 400 cm
Ultrasonic Sensor
LED Blink
No Change
If distance < 3 cm
If distance > 3 cm

## Slide 11
Video Demonstration